### WEB INFO
Material that distributors can use on their websites.

### PowerCable 2PZ

PowerCable 2KZ is FLAT PDU (Power Distribution Unit) for remote power control (remote restarting).  Device connectivity is LAN or WiFi, 2 power outputs (110/230V max 16A) are available on terminal blocks.

NETIO PowerCable 2PZ is flat PDU with LAN connectivity using a RJ45 (Ethernet) or WiFi (2.4 GHz – internal antenna).

Both power outputs can be individually switched On/Off (restarted - short off) on the device website, Mobile App or from the NETIO Cloud service web.

PowerCable 2PZ PDU supports a week-based scheduler feature.

PowerCable 2PZ we call “FLAT PDU” because can be installed behind TV, under double ceiling or to similar limited space. 2PZ is delivered without power cables, user have to install power cables to the terminal block with using screw driver.

Open API enables integration into third-party systems using a wide range of protocols (JSON, Modbus/TCP, XML, SNMP, MQTT, Telnet, ..).

With the NETIO Cloud service, the output(s) can be switched On/Off from anywhere. The NETIO Cloud service, provided for a fee, uses SSL/TLS security and servers in Europe.

AV drivers make it easy to connect NETIO sockets to professional Audio/Video control systems such as RTI, ELAN, SAVANT, BrightSign, Crestron, Control4 etc.

- LAN + WiFi connectivity

- WEB interface: Yes

- Power control: 2 Outputs (max 110-230V AC / 16A)

- Power metering: none

- OPEN API: MQTT-flex, Modbus/TCP, Telnet, JSON, XML, SNMP, ..

- Service: NETIO Cloud (with TLS security)

- Mobile App: NETIO Mobile 2 (Android & iOS)

#### Use cases for the remote restarting

- Remote restart (over the Web, Cloud, Mobile App)

- Energy savings (scheduler)

- TV screens, projectors

- Powering Machines, lights, Audio system.

- 3rd party AV system controlling power outputs (Crestron, Control4, RTI, BrightSign)

Using Condition & Rules / PAB it is possible to define power output(s) reaction to daylight time, Power-Up, ping answer etc...

#### Open API

The NETIO PowerCable 2PZ outputs can be controlled over the Web and the NETIO Cloud at the same time. For Open API communication, one M2M protocol can be chosen from among the following:

- Modbus/TCP

- MQTT-flex

- Telnet

- URL API (http get)

- JSON over HTTP

- XML over HTTP

- SNMP v1

- SNMP v3

- HTTP(s) Push JSON

- HTTP(s) Push XML

Documentation for the protocols is available at the manufacturer’s website. The ANxx Application Notes provide useful deployment guidance.

Regardless of which Open API protocol is being used, the PDU can always be controlled from its web interface and from the NETIO Cloud service at the same time.

Device variants

- PowerCable 2PZ: plain unit (with terminal block connector inside), no power cables included.

Industrial product quality

- PowerUp state – the state of the outputs after the device is powered up is configurable (On/Off/Last).

- ZVS – for switching an appliance on and off more frequently than a few times a day, ZVS (Zero Voltage Switching) support becomes important in the long term.

#### Scheduler function (calendar)

With the Scheduler function, each output can be switched on and off automatically at pre-defined times and days-of-week. A schedule is useful for saving energy and periodic restarts of other equipment.

WiFi connectivity only

For WiFi setup without LAN, the product features a built-in WiFi AP as well as a wizard to guide you through the selection of a WiFi network and configuring the connection.

### Technical Specifications

#### NETIO PowerCable 2PZ

- LAN (RJ45): Yes

- WiFi: Yes

- Web: Built-in web server

- Online demo: Yes

- FW upgrade: Yes - web

- Mobile app: NETIO Mobile2 (LAN + Cloud)

- Installation without a Cloud connection: Yes

- Control button: Yes

- Service: NETIO Cloud (for a fee)

- M2M API protocols:

  - JSON over HTTP (default)

  - MQTT-flex (extended MQTT, SSL enabled)

  - HTTP Push JSON

  - HTTP Push XML

  - SNMP v1

  - SNMP v3

  - Modbus/TCP

  - XML over HTTP

  - URL API (http get) (writing only)

  - Telnet (Outputs only, backwards compatible with KSHELL)

- Lua scripting support: No

- Condition & Rules: Yes

- Scheduler function (weekly calendar): Yes

- IP (ping) WatchDog function: Yes (Condition & Rules)

- Power WatchDog function: No

- Sending e-mails: No

- Power input: Terminal block (2.5mm2), 100-240VAC (50/60Hz) / max 16A

- Power output: Terminal block (2.5mm2)

- Metered outputs: none

- Power outputs: 2x Relay + ZVS (Out 1, 2: SPST-NO) – Max 16A

- DI (Digital Inputs): none

- Internal consumption: Max 2 W

- SPD – surge protection: Yes, type 3

- ZVS (Zero Voltage Switching): Yes

- IOC (output state independent from FW updates): Yes

- PowerUp state of outputs: On / Off / LAST state

- Mechanical characteristics: 102 x 32 x 149 mm

- Protection: IP20

- Sound output: No

- Temperature range: -20°C to +55°C

- AV Drivers (most popular):

  - BrightSign

  - Control 4

  - Crestron

  - ELAN

  - Kramer

  - Loxone

  - Neets / biamp

  - RTI

  - SAVANT

  - SKAARHOJ

More information about this product: 
https://www.netio-products.com/en/device/powercable-2pz

#### YouTube Video

https://youtu.be/QbfY2yu_S-M

You can use this as embedded YouTube video on your website (webshop).

### Keywords

PowerCable 2PZ, 2 channels flat PDU, wifi energy PDU, LAN IO, Web control, NETIO Cloud, Open API, zero voltage switching, ZVS, JSON, Modbus-TCP, SNMP, MQTT, Telnet, SSL/TLS security, scheduler, LAN Ethernet interface, remote restarting